## Slide 1: Computer Architecture and Operating Systems Lecture 1: Introduction
Andrei Tatarnikov
andrewt0301@gmail.com
@andrewt0301

## Slide 2: Course Resources
Website
https://andrewt0301.github.io/hse-acos-course/
Wiki
http://wiki.cs.hse.ru/ACOS_DSBA_2022/2023
http://wiki.cs.hse.ru/ACOS_COMPDS_2022/2023
Telegram
https://t.me/+8sj1n_GbjBFjYWUy (DSBA)
https://t.me/+fFSXHDh_nP8wNTM6 (COMPDS)

## Slide 3: Course Team
Andrei Tatarnikov
Assistants
Instructors
Alexey Kanakhin
Alexandra Borisova
Oleg Malchenko
Andy Xu
Nikolay Chechulin
Vladislav Kirichok
Daria Lapko
Artem Borisov
Igor Mineev

## Slide 4: Course Outline
Syllabus (see the web site for details)
Module 3: Computer Architecture
  Computer architecture
  Assembly language programming (RISC-V)
  Home works, quizzes, and test
Module 4: Operating Systems
  Operating System Architecture (Linux)
  System programming in C
  Home works, quizzes, and test
Final Exam

## Slide 5: Course Motivation
Increase your computer literacy
Have an idea how computers under the hood
Better understand performance
Be familiar with system programming
Be familiar with system tools

## Slide 6: Example: Matrix Multiplication (part 1)
import random from time import time n = 1024
A = [[random.random() for row in range(n)] for col in range(n)] B = [[random.random() for row in range(n)] for col in range(n)] C = [[0 for row in range(n)] for col in range(n)] start = time() for i in range(n): for j in range(n): for k in range(n): C[i][j] += A[i][k] * B[k][j] end = time() print('%0.6f' % (end - start))
Python
Floating-point operations:
=
Running time:
503.130450 sec.
Performance:
~ 4,27 MFLOPS

## Slide 7: Example: Matrix Multiplication (part 2)
public class Matrix { static int n = 1024; static double[][] A = new double[n][n]; static double[][] B = new double[n][n]; static double[][] C = new double[n][n];
public static void main(String[] args) { java.util.Random r = new java.util.Random(); for (int i = 0; i < n; i++) { for (int j = 0; j < n; j++) { A[i][j] = r.nextDouble(); B[i][j] = r.nextDouble(); C[i][j] = 0; } } long start = System.nanoTime(); for (int i = 0; i < n; i++) { for (int j = 0; j < n; j++) { for (int k = 0; k < n; k++) { C[i][j] += A[i][k] * B[k][j]; } } } long stop = System.nanoTime(); System.out.println((stop - start) * 1e-9); } }
Java
Floating-point operations:
=
Running time:
12.946224 sec.
Performance:
~ 165 MFLOPS

## Slide 8: Example: Matrix Multiplication (part 3)
#include <stdlib.h> #include <stdio.h> #include <sys/time.h>
#define n 1024 double A[n][n]; double B[n][n]; double C[n][n];
float tdiff(struct timeval *start, struct timeval *end) { return (end->tv_sec - start->tv_sec) +
1e-6*(end->tv_usec - start->tv_usec); } int main(int argc, const char *argv[]) { for (int i = 0; i < n; i++) { for (int j = 0; j < n; j++) { A[i][j] = (double)rand() / (double)RAND_MAX; B[i][j] = (double)rand() / (double)RAND_MAX; C[i][j] = 0; } } struct timeval start, end; gettimeofday(&start, NULL); for (int i = 0; i < n; i++) { for (int j = 0; j < n; j++) { for (int k = 0; k < n; k++) { C[i][j] += A[i][k] * B[k][j]; } } } gettimeofday(&end, NULL); printf("%0.6f\n", tdiff(&start, &end)); return 0; }
C Language
Floating-point operations:
=
Running time:
13.714264 sec.
Performance:
~ 153 MFLOPS

## Slide 9: Example: Matrix Multiplication (part 4)
C Language: Optimizations
Loop order: i, j, k
for (int i= 0; i < n; i++) { for (int j= 0; j < n; j++) { for (int k= 0; k < n; k++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Loop order: i, k, j
for (int i= 0; i < n; i++) { for (int k= 0; k < n; k++) { for (int j= 0; j < n; j++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Loop order: j, k, i
for (int j= 0; j < n; j++) { for (int k= 0; k < n; k++) { for (int i= 0; i < n; i++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Running time:
13.714264 sec.
Performance:
~ 153 MFLOPS
Running time:
2.739385 sec.
Performance:
~ 795 MFLOPS
Running time:
19.074106 sec.
Performance:
~ 113 MFLOPS

## Slide 10: Example: Matrix Multiplication (part 5)
Feature | Specifiction
Model | MacBook Pro 9,1
Processor Name | Quad-Core Intel Core i7
Processor Speed | 2,3 GHz
Number of Processors | 1
Total Number of Cores | 4
Floating-Point Operations per Cycle | 4
L2 Cache (per Core) | 256 KB
L3 Cache: | 6 MB
Hyper-Threading Technology | Enabled
Memory | 8 GB
Peak = () * 1 * 4 * 4 = 36 800 MFLOPS

## Slide 11: What affects performance?
Hardware/Software Component | How It Affects Performance
Algorithm | Determines both the number of source-level statements and the number of I/O operations executed
Programming Language, Compiler, and Architecture | Determines the number of computer instructions for each source-level statement
Processor and Memory System | Determines how fast instructions can be executed
I/O System (Hardware and Operating System) | Determines how fast I/O operations may be executed

## Slide 12: History: 0th Generation – Mechanical
1834–71: Analytical Engine designed by Charles Babbage
Mechanical gears, where each gear represented a discrete value (0-9)
Programs provided as punched cards
Never finished due to technological restrictions

## Slide 13: History: 1st Generation - Vacuum Tubes
1945–55: first machines were created (Atanasoff–Berry, Z3, Colossus, ENIAC)
All programming in pure machine language
Connecting boards and wires, punched cards (later)
Stored program concept
Input
Output
Memory
Arithmetical / Logic Unit
Control Unit

## Slide 14: History: 2nd Generation - Transistors
1955–65: era of mainframes (e.g. IBM 7094) used in large companies
Programming in assembly language and FORTRAN
Batch systems (IO was separated from calculations)
Punched cards and magnetic tape
Loaders (OS ancestors)

## Slide 15: History: 3rd Generation – Integrated Circuits
1965–1980: computer lines using the same instruction set architecture (e.g. IBM 360)
First operating systems (e.g. OS/360, MULTICS)
Multiprogramming and timesharing
Computer as utility
Programming languages and compilers (LISP, BASIC, C)
Job 3
Job 2
Job 1
Operating
System
Memory Partitions

## Slide 16: History: 4th Generation – VLSI and PC
1980–Present: personal computers, laptops, servers (Apple, IBM, etc.)
Architectures: x86-64, Itanium, ARM, MIPS, PowerPC, SPARC, RISC-V, etc.
Operating systems: UNIX (System V and BSD), MINIX, Linux, MacOS, DOS, Windows (NT)
ISA (CISC, RISC, VLIW), caches, pipelines, SIMD, vectors, hyperthreading, multicore

## Slide 17: History: 5th Generation – Mobile devices
1990–Present: mobile devices, embedded systems, IoT devices
Custom processors and FPGAs
Mobile operating systems: Symbian, iOS, Android, Windows Mobile
Real-time operating systems

## Slide 18: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Memory capacity
Year | Technology | Relative performance/cost
1951 | Vacuum tube | 1
1965 | Transistor | 35
1975 | Integrated circuit (IC) | 900
1995 | Very large scale IC (VLSI) | 2,400,000
2013 | Ultra large scale IC | 250,000,000,000

## Slide 19: Moore’s Law
Gordon Moore (1929-...) cofounded Intel in 1968 with Robert Noyce
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Limited by power consumption
Slowed down since 2010

## Slide 20: Single Core Performance
Constrained by power, instruction-level parallelism, memory latency
Move to multicore

## Slide 21: Power Trends

## Slide 22: Memory Performance Gap

## Slide 23: Current Challenges
Single core performance improvement has ended
  More powerful microprocessor might not help
Memory-efficient programming
  Temporal locality
  Spatial locality
Parallelism to improve performance
  Data-level parallelism
  Thread-level parallelism
  Request-level parallelism
Performance tuning require changes in the application

## Slide 24: Concluding Remarks
To create software that efficiently deals with big data, we need to understand how hardware is organized and managed by operating system
  Computer architecture
  Assembly language
  Compiler basics
  Operating systems
Focus
of this course

## Slide 25: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero