## Slide 1: Computer Architecture and Operating Systems Lecture 4: Instruction Set Architecture
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: How Computer Works
Computer
Main Parts:
Control
Datapath
Memory
Input
Output
CPU
Memory
Devices
Input
Output
Control
“Brain”
Datapath
Registers
Bus

## Slide 3: Stored Program Concept
32-bit instructions and data stored in memory
Program is a sequence of instructions
To run a new program:
  Simply load the new program into memory
Program Execution:
  CPU fetches (reads) instructions from memory in sequence
  CPU performs the specified operations

## Slide 4: Stored Program Representation
Assembly Code
lw t0, 32 (t1)
add s1, s0, s2
addi t0, s3, -12
sub t0, t3, t5
Machine Code
0x02032283
0x012404B3
0xFF498293
0x41EE02B3
Memory
Stored Program
Address
…
0x00400000
0x00400004
0x00400008
0x0040000С
…
Instructions
…
0x02032283
0x012404B3
0xFF498293
0x41EE02B3
…
Program Counter (PC): keeps track of current instruction

## Slide 5: Memory Layout
Text: program code
Static data: global variables
  E.g., static variables in C, constant arrays and strings
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
Stack
Dynamic Data
Static Data
Text
Reserved
PC = 0x 0040 0000
0
GP = 0x 1000 8000
SP = 0x 7FFF EFFC

## Slide 6: RISC-V Instructions
Name | Description | Version | Status
Base |  |  | 
RVWMO | Weak Memory Ordering | 2.0 | Ratified
RV32I | Base Integer Instruction Set, 32-bit | 2.1 | Ratified
RV64I | Base Integer Instruction Set, 64-bit | 2.1 | Ratified
RV128I | Base Integer Instruction Set, 128-bit | 1.7 | Open
Extensions |  |  | 
M | Standard Extension for Integer Multiplication and Division | 2.0 | Ratified
A | Standard Extension for Atomic Instructions | 2.1 | Ratified
F | Standard Extension for Single-Precision Floating-Point | 2.2 | Ratified
D | Standard Extension for Double-Precision Floating-Point | 2.2 | Ratified
G | Shorthand for the base integer set (I) and above extensions (MAFD) | N/A | N/A
Q | Standard Extension for Quad-Precision Floating-Point | 2.2 | Ratified
C | Standard Extension for Compressed Instructions | 2.0 | Ratified
ZiCSR | Control and Status Register (CSR) | 2.0 | Ratified
Zifencei | Instruction-Fetch Fence | 2.0 | Ratified
And more standard and custom extensions… |  |  | 

## Slide 7: Design Principles
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
Design Principle 2: Make the common case fast
  Most common cases affect the performance the most
Design Principle 3: Smaller is faster
  32 registers, fewer instructions
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible

## Slide 8: Six Instruction Formats
R-format: instructions using 3 register inputs
  add, xor, mul - arithmetic/logical ops
I-format: instructions with immediates, loads
  addi, lw, jalr, slli
S-format: store instructions
  sw, sb
SB-format: branch instructions
  beq, bge
U-format: instructions with upper immediates
  lui, auipc - upper immediate is 20-bits
UJ-format: the jump instruction
  jal

## Slide 9: R-format Instructions
Arithmetic Instructions
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1 and rs2: first and second source register 5-bit numbers
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
add x9, x20, x21
0000 0001 0101 1010 0000 0100 1011 0011two = 015A04B316
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 10: I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
0x123
6
5
0
19
000100100011
00110
00101
000
0010011
addi t0, t1, 123
0001 0010 0011 0011 0000 0010 1001 0011two = 0x1233029316

## Slide 11: S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
imm[11:5]
rs2
rs1
imm[4:0]
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
5
6
4
2
35
0000000
00101
00110
00100
010
100011
sw t0, 4(t1)
0000 0000 0101 0011 0010 0010 0010 0011two = 0x0053222316

## Slide 12: SB-format Instructions
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Branch range is +/- 4KB
PC-relative addressing
  Target address = PC + immediate × 2
imm[10:5]
rs2
rs1
imm[4:1]
funct3
opcode
imm[12]
imm[11]
0
1
0
0
99
0
0
2
000000
00001
00000
000
1100011
0
0
0010
beq x0, x1, 0x4
0000 0000 0001 0000 0000 0010 0110 0011 two = 00100263 16
5 bits
5 bits
3 bits
7 bits
5 bits
6 bits
1 bit
1 bit

## Slide 13: U-format Instructions
Upper-immediate values: 20-bit values shifted left by 12 bits
  opcode: operation code
  rd: destination register number
  imm: 20-bit immediate value
imm[31:12]
rd
opcode
20 bits
5 bits
lui x5, 0x12345
0001 0010 0011 0100 0101 0010 1011 0111two = 123452b716
0x12345
5
55
0001 0010 0011 0100 0101
00101
0110111

## Slide 14: UJ-format Instructions
rd
opcode
imm[11]
imm[20]
imm[19:12]
imm[10:1]
7 bits
5 bits
10 bits
8 bits
1 bit
1 bit
5
111
0
0
0
2
00101
1101111
0
0
00000000
0000000010
Jump instructions
  opcode: operation code
  rd: destination link register
  imm: signed offset in multiples of 2 bytes added to PC
  Target address = PC + immediate × 2
  Jump range is +/- 1MB
0000 0000 0100 0000 0000 0010 1110 1111two = 004002ef16
jal x5, 0x4

## Slide 15: RISC-V Addressing Summary

## Slide 16: RISC-V Encoding Summary

## Slide 17: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero