## Slide 1: Computer Architecture and Operating Systems Lecture 11: Exceptions
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Exceptions and Interrupts
Exception is an unscheduled event that disrupts program execution
  Arises within the CPU
    e.g., undefined opcode, system call, …
Interrupt is an exception that comes from outside of the processor
  From an external I/O controller
Some architectures use the term interrupt for all exceptions
Exceptions require special system instructions and registers
Dealing with exceptions without sacrificing performance is hard

## Slide 3: Control and Status Registers
Control and Status Registers (CSRs) are system registers provided by RISC-V to control monitor system states
CSR’s can be read, written and bits can be set/cleared
Each CSR has a special name and is assigned a unique function.
In this course, we focus on the user privilege level
We will use user-level CSRs to handle user-level exceptions

## Slide 4: Main CSR Registers
User Trap Setup
  ustatus – User status register
  uie – User interrupt-enable register
  utvec – User trap handler base address
User Trap Handling
  uscratch – Scratch register for user trap handlers
  uepc – User exception program counter
  ucause – User trap cause
  utval – User bad address or instruction
  uip – User interrupt pending

## Slide 5: System Instructions
ebreak – Pause execution (at a breakpoint)
ecall – Execute a system call specified by value in a7
uret – Return from handling an interrupt (to uepc)
wfi – Wait for interrupt
csrrc, csrrci, csrrs, csrrsi, csrrw, csrrwi – Read/write CSR

## Slide 6: Handling Exceptions in CPU
Save PC of offending (or interrupted) instruction
  In RISC-V: User Exception Program Counter (UEPC)
Save indication of the problem
  In RISC-V: User Exception Cause Register (UCAUSE)
  32 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 1C09 0000hex

## Slide 7: Handling Vectored Exceptions in CPU
Alternate Mechanism: Vectored Interrupts
  Handler address determined by the cause
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
  …: …
Handler instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 8: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  Use UEPC to return to program
Otherwise
  Terminate program
  Report error using UEPC, UCAUSE, …

## Slide 9: Trivial Exception Handler
# Example with a trivial exception handler that just returns to the next instruction.
.text
j main
handler:
# Just ignore it by moving uepc to the next instruction
csrrw t0, uepc, zero # load exception PC into t0
addi t0, t0, 4 # increment t0
csrrw zero, uepc, t0 # update exception PC
uret # return to uepc
main:
la t0, handler
csrrw zero, utvec, t0 # set utvec (5) to the handlers address
csrrsi zero, ustatus, 1 # set interrupt enable bit in ustatus (0)
lw zero, 0(zero) # trigger trap for Load access fault
li a7, 10
ecall

## Slide 10: Exceptions in a Pipeline
Another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set SEPC and SCAUSE register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 11: Pipeline with Exceptions

## Slide 12: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in SEPC register
  Identifies causing instruction

## Slide 13: Exception Example
Exception on add in
  40 sub x11, x2, x4 44 and x12, x2, x5 48 orr x13, x2, x6 4c add x1, x2, x1 50 sub x15, x6, x7 54 ld x16, 100(x7) …
Handler
  1C090000 sd x26, 1000(x10) 1c090004 sd x27, 1008(x10) …

## Slide 14: Exception Example

## Slide 15: Exception Example

## Slide 16: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 17: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 18: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero